## Slide 1: Physics 101
jodavis42@gmail.com

## Slide 2: Intro to Game Physics
All about making believable interactions
Approximate real world for speed and stability
Focusing on Rigid Body dynamics and 2D
*Physics engines are (kinda) hard
Notes: This presentation is all about the basics of making a game physics engine. An important realization of this is what does game physics entail. In particular, game physics is all about making believable interactions that aren’t necessarily accurate. Most physics engines are still very realistic, but many assumptions are commonly made for the sake of performance or even stability. The biggest approximation I’ll make for this entire presentation is that we’ll only work with rigid bodies. This means objects that cannot deform. This simplifies a ton of math and it’s not worth even looking at deformations if you’ve never done a physics engine.
This presentation will also focus on 2D, since it’s an intro, with small bits of 3D references thrown in.
One quick thing I want to elaborate on is that physics can be very difficult and taxing (depending on how advanced you go) but they can be super rewarding!

## Slide 3: Basic Physics Components
Collider
RigidBody
PhysicsSpace
Notes: Before going into any more technical details I need to cover a common high-level architecture of a physics engine. This is important as we need to know where certain data lives. This is based on what I did in Zero but heavily simplified.

## Slide 4: Collider
Defines a shape that can be collided with (defines surface/volume)
Bounding volumes typically stored here (Aabb)
Different shapes are derived classes:
struct BoxCollider : public Collider
{
Vector2 mSize;
};
struct SphereCollider : public Collider
{
float mRadius;
};
Notes: The Collider class is used to define the shape and size of an object for collision detection. A collider by itself typically doesn’t have too much meaning (more properties in a bit) as derived classes are used to define actual useful shapes. The most common are a Box and Sphere Collider, each defining their own properties to define a volume and surface.

## Slide 5: Collider – Material Properties
Material properties needed to define dynamics
*Commonly grouped together in a material
struct PhysicsMaterial
{
float mFriction; //[0, ]
float mRestitution;//[0,1]
float mDensity; //[0, ]
};
Notes: Since a collider represents a surface, it usual stores various surface properties about an object. There’s three common properties that a Collider needs to define:
1. Friction is used to describe how resistant objects are to motion when sliding along the surface of another. Friction is commonly stored as just one value (set dynamic and static friction to the same).
2. Restitution describes how ‘bouncy’ an object is. This is a 0 to 1 scalar where 0 is no elasticity and 1 is perfect elasticity.
3. Density is used to compute the mass of an object. Mass will be a property of RigidBody (more in a moment) but it’s fairly common to store density on a collider when you get to more advanced architecture (multiple colliders per body). As mass is defined as it makes sense that a collider’s volume is needed along with a density to compute mass.
These material properties are commonly grouped together in a material so that data can be shared both saving memory and making it easier to change lots of objects at once.
Finally, any additional properties about collision detection are stored here. The most common one is a ghost flag for making trigger regions.
Since a collider represents a surface, it usual stores various surface properties about an object. There’s three common properties that a Collider needs to define:
1. Friction is used to describe how resistant objects are to motion when sliding along the surface of another. Friction is commonly stored as just one value (set dynamic and static friction to the same).
2. Restitution describes how ‘bouncy’ an object is. This is a 0 to 1 scalar where 0 is no elasticity and 1 is perfect elasticity.
3. Density is used to compute the mass of an object. Mass will be a property of RigidBody (more in a moment) but it’s fairly common to store density on a collider when you get to more advanced architecture (multiple colliders per body). As mass is defined as 𝑚𝑎𝑠𝑠=𝑑𝑒𝑛𝑠𝑖𝑡𝑦∗𝑣𝑜𝑙𝑢𝑚𝑒 it makes sense that a collider’s volume is needed along with a density to compute mass.
These material properties are commonly grouped together in a material so that data can be shared both saving memory and making it easier to change lots of objects at once.
Finally, any additional properties about collision detection are stored here. The most common one is a ghost flag for making trigger regions.

## Slide 6: Collider – Gameplay Properties
Properties very common for gameplay logic:
struct Collider
{
// Gameplay properties
bool mIsGhost;
bool mSendsEvents;
u32 mCollisionFlags;
};
Notes: Some additional gameplay logic flags are very common to define too.
Ghost is used to make a collider behave like a trigger region. A ghost object will detection collision but skip resolution (more later).
This is a less common property that you can probably skip, but it’s not uncommon to have a flag to turn off even sending (collision notifications). This is sometimes done for performance, but is most often needed to help filter out important messages for gameplay.
Some kind of collision flag system is often needed to skip resolution (and sometimes detection) between certain kinds of objects. These systems can be as simple or complex as you want. The simplest is to define an id and only check objects if they share an id. A more complicated system involves a bit flag mask where an object can be in multiple ‘ids’ at once. In this case two objects only collide if they binary and to a non-zero value. Zero uses a collision group and table system to abstract this even further, allowing interactions between ids to be defined (basically an abstraction on the bit flags approach)

## Slide 7: RigidBody
RigidBody gives an object inertia (mass + velocity)
struct RigidBody
{
float mInvMass;
float mInvInertia;
Vector2 mLinearVelocity;
float mAngularVelocity;
Vector2 mLinearForce;
float mAngularForce; //Torque
u32 mStateFlags; // Static/Kinematic
};
Notes: RigidBody gives an object inertia, that is it gives the object mass which allows it to move via forces. Almost every value is broken up into two pieces on a RigidBody, a linear and angular portion.
Mass: Mass defines how resistant an object is to change in movement. The inverse mass is normally stored as it’s very common to divide by mass in equations. An additional benefit of this is that an inverse mass of zero is equivalent to infinite mass and all of the math will work out as if the object can’t be moved. Parallel to mass is the inertia which is used to define the resistance to rotational movement. These are both typically derived from a collider’s density and volume, but can also be manually set depending on how you want to structure your engine.
Velocity and Force are fairly simple properties that simply define the current movement of an object.
Finally, some additional gameplay flags are needed. The most common is a way to change a RigidBody between dynamic and static (infinite mass). Beyond these two, there’s typically a third state for dynamics called kinematic. A kinematic is an ‘infinite mass mover’. This is basically a static object that doesn’t assume it’s stationary. This is very common for players so it’s something I recommend looking into right away. I won’t really go into much detail in this presentation, but to make a kinematic object you basically need to somehow provide a velocity to all of resolution whenever this object moves. There’s a lot of different approaches here between how this works though. Ask if you have questions.

## Slide 8: Collider and RigidBody
A normal object has a collider and rigid body
  Has a collision volume and inertia so it can move
  Logical implications if one isn’t present
  Up to you to choose any dependencies (can be a lot to manage)
Notes: I want to briefly talk about the Collider and RigidBody pairing. With these two components defined we can derive a few different meanings from the presence or absence of these components.
The most common configuration is an object having both components. In this case the object has surface which allows collision detection and inertia which allows force and collision and response. This object moves about and interacts in a scene freely.
It’s not uncomment to either group these two together or form a dependency chain (e.g. RigidBody depends on Collider), but by keeping them separate a few logical states arise:
A Collider with no RigidBody is a static object (e.g. infinite mass) that can be collided with but can’t be moved. This is very common for terrain or static geometry in the world
A RigidBody with no Collider is a bit more odd. This is effectively a point mass that can move around with forces but can’t interact with anything. This is less common but when you get into more advanced architecture or gameplay features this can be nice.
I don’t have any strong recommendations for how to structure this depending on how advanced you want to make your engine. Forming dependencies makes a lot of logic easier to write but at the cost of some flexibility.

## Slide 9: PhysicsSpace
A space where objects can interact together
Can define space parameters (gravity)
Defines the core update loop
Additionally provides “query” functions (raycasting)
Super important for your team!
Notes: Finally is the physics space component. We’ll be spending the most time talking about this as it’s where the core update loop happens and hence the majority of the game logic and math is defined. The other components mostly just define properties that the space consumes.
Beyond defining the update loop and containing a bunch of objects, the physics space also contains a few properties. While not done this way in Zero, this is a fairly good place to store scene-wide parameters like gravity or drag coefficients. Beyond these, most flags on a space tend to be for the physics developer to easily tweak or debug and not as much for end-users.
The other common thing for a physics space to define is a bunch of helper functions needed for gameplay. The only one I’ll talk on in detail (more later) is query functions, in particular raycasting. The idea is that gameplay often needs to ask “what does this shape hit”. This is one of those features that you’ll make that is not for you but for everyone else on your team.

## Slide 10: Types of Physics
Discrete vs. Continuous
Discrete: Picture flip-book
Do discrete!
Some artifacts but significantly easier and more robust!
*If you haven’t implemented discrete don’t attempt continuous
Notes: Before getting into the core physics loop there’s one important point I need to talk on first, and that’s what kind of a physics engine we’re writing. There’s two main distinctions in a rigid body based physics engine: discrete and continuous collision. These mostly are described in terms of collision detection but they end up affecting the entire pipeline.
Discrete collision detection can be thought of as a picture flip-book where objects teleport from frame-to-frame. In this system we simply look at the end of the frame to perform detection. This has the problem that we don’t detect collisions until after they happen and some collisions can be entirely missed (tunneling). Continuous collision detection fixes this by evaluating the full values of the frame.
Continuous is obviously “better” but you should not even attempt it. Discrete is 100% the way you should go as it’s significantly easier to implement, it’s good enough for everything you’ll be doing (most likely), and will actually be more stable and robust than the “better” continuous method.
I can speak to this one firsthand. I made this mistake my sophomore year and spent the first semester fixing weird bugs and other issues. I replaced my entire first semester’s work with a discrete engine that was way more stable and faster in about two weeks. Most commercial game engines are also (primarily) discrete so it’s good enough for everyone else too. There are places for continuous, but if you haven’t done a discrete engine first then you’re basically bound for failure if you try continuous.

## Slide 11: Basic Physics Pipeline
Integration – Update Force/Velocity/Position
Collision Detection – Find what’s colliding and where
Collision Resolution – Apply collision response
Publishing – Tell everyone what happened
Notes: The core physics update loop is broken up into 4 main concepts.
These four steps should be thought of as distinct phases that completely finish and then transfer data to the next phase.

## Slide 12: Integration
Two sub-steps:
  Velocity Integration: Acceleration -> Velocity
  Position Integration: Velocity -> Position
Lots of integration techniques:
  Explicit Euler
  Semi Implicit Euler
  Implicit Euler
  Verlet
  RK4
  Etc…
Notes: Integration is the process of updating position and velocity (e.g. actual numerical techniques of performing an integral on velocity). This is broken up into two sub-integration steps:
Velocity Integration: acceleration (remember ) is integrated to update velocity. For instance, you have gravity and other forces being applied to an object so how do we update velocity?
Position Integration: velocity is integrated to update position.
There’s a ton of different integration techniques out there, all with their different trade-offs.
Integration is the process of updating position and velocity (e.g. actual numerical techniques of performing an integral on velocity). This is broken up into two sub-integration steps:
Velocity Integration: acceleration (remember 𝐹=𝑚𝑎) is integrated to update velocity. For instance, you have gravity and other forces being applied to an object so how do we update velocity?
Position Integration: velocity is integrated to update position.
There’s a ton of different integration techniques out there, all with their different trade-offs.

## Slide 13: Integration
Explicit Euler
Semi-implicit Euler
Do semi-implicit!
Notes: For almost all rigid body simulations, the Euler integration techniques are used. This is because they’re incredibly fast and good enough.
You’ve probably seen both the explicit and semi-implicit Euler techniques before. These techniques might look really similar but there’s one key difference between them: the order they’re updated. In explicit Euler, position is integrated before velocity. This means the last frame’s velocity is used to update position. In semi-implicit Euler the velocity is integrated before position. This means the new velocity from this frame is used to update position.
This might seem like a subtle difference, but it’s very important. Without getting into too much detail explicit Euler will add energy to your simulation and semi-implicit will take away energy. For games, explicit Euler is typically the worst choice and you should never use it (it adds energy). The current industry standard (AAA games even) is to use semi-implicit Euler.
The above pictures show a very simple n-body force simulation (planet gravity). Notice that in the explicit Euler simulation the orbiting body gets further away until it’ll eventually fly off. However, notice the semi-implicit Euler maintains a perfect circular orbit.
As a note, you ‘need’ better integration when forces are dependent on position, like spring systems.

## Slide 14: Collision Detection
Broken up into three main phases:
  BroadPhase:
    All object -> Pairs of objects
  MidPhase (optional):
    pairs of objects -> pairs of primitives
  NarrowPhase:
    pairs of primitives -> intersecting pairs
Notes: After integration comes the collision detection pipeline. The goal of this phase is to find out what objects collide and where.
There’s commonly two steps in collision detection but occasionally a third phase can exist. At a high-level, each phase reduces the collection of objects into a smaller sub-set of pairs.

## Slide 15: Collision Detection - BroadPhase
Coarse high-level detection
  The best optimization is to do nothing
Find possible pairs (returns false-positives)
A
D
B
C
E
Resultant pairs: [A-D], [B-D], [C-E]
Notes: Broad-phase is a coarse high-level approximation of collision detection. The idea is that the best optimization is to not do something if you don’t have to. We’ll see in a bit, but narrow-phase is a lot more expensive than broad-phase so we want to limit what can get there.
Typically, broad-phase will take all of the objects in your scene and return possible pairs that could collide. To be fast, broad-phase does approximations that will efficiently reject possible pairs but will return false positives. A good example is wrapping each object in an Aabb and checking collision with that (pictured above). An Aabb check is very cheap but isn’t accurate to most shapes.
Note: broad-phase can return false positives but can never produce false negatives (e.g. it can’t miss anything).

## Slide 16: Collision Detection - BroadPhase
My recommendation:
Start with Aabb n-squared:
Easy to implement
Hard to get wrong
If needed, switch to dynamic aabb tree
“Best” all-purpose spatial partition
Notes: As this is an optimization I wouldn’t recommend doing too much to start with broad-phase. If you spend a lot of time optimizing your collision detection but you don’t have resolution then you’ve wasted your time. Because of this I recommend starting with something simple that can be easily swapped out later (think virtual interface). In particular, I recommend starting with an n-squared aabb spatial partition. This is simply iterating over all objects in an n-squared fasion (double for loop) and just checking if their aabbs intersect first. This isn’t great but it’s a huge improvement over n-squared.
If this is good enough for your game and you’re not particularly interested in doing more then I’d recommend stopping here. If you need some speed improvements here I’d recommend looking into a dynamic aabb tree. I’m very biased towards this broad-phase but for good reason. It’s not the best, but it’s very good and not too hard to write.
Don’t worry, you’ll have to do more when you get to my class anyways (CS350)

## Slide 17: Collision Detection - NarrowPhase
Determines if two primitive pairs intersect
Typically some kind of table for possible shapes:
  Aabb/Aabb
  Sphere/Sphere
  Aabb/Sphere
  Etc…
Simple shapes tend to have hand-written tests
For generic stuff look at SAT/GJK
Notes: Narrow-phase is the very last stage in the collision detection pipeline. It’s job is to accurately determine if two primitives intersect and if so where. This stage is not allowed to return false-positives.
Typically narrow-phase is effectively a wrapper around a bunch of individual collision test functions such as Aabb vs. Aabb and Sphere vs. Sphere. This is easy to implement as a table of calls or a double dispatch pattern.
Getting into actual collision detection algorithms is beyond the scope of what I can cover today, so I’ll leave this up to you to research. For a simple game you’d just need to do a few simple primitive tests between sphere, aabb, and maybe triangles. If you want to get more advanced at some point I’d recommend looking into either SAT or GJK.

## Slide 18: NarrowPhase - ContactManifold
Resolution needs information about how objects collided
struct Manifold
{
struct ContactPoint
{
Vector2 mPointA;
Vector2 mPointB;
float mPenetration;
};
Vector2 mNormal; // From A to B
Array<ContactPoint> mContactPoints;
};
Notes: Right after narrow-phase will be resolution which will deal with object intersections, but to do this resolution will need information about how objects are intersecting. This means that narrow phase needs to return not only if objects intersect, but how they are intersecting.
This is data is often grouped into a structure called a manifold which consists of three primary pieces of data:
The normal defines the axis for resolution to solve on. This should be the axis that requires the least effort to push the objects apart on (minimum translational distance)
Penetration describes how much the objects are overlapping (how much error discrete allowed). This is needed to fix overlap and push objects apart.
Contact points (typically broken up into points on each object) are needed when rotation is involved in order to figure out where to apply “force” which will result in both linear and angular movement.
Generating a contact manifold is probably the hardest part of narrow-phase to get right. There’s a lot of tricky math, but one small thing to be careful of (more later) is that data needs to be consistent, in particular we’ll need to make sure the normal direction doesn’t randomly flip around. The most common way to do this is to define the normal as always point from one object towards the other which can be enforced with a simple dot-product check.

## Slide 19: NarrowPhase - Generic
Simple shapes tend to have hand-written tests
Two common generic algorithms:
SAT
  Easy to understand
  Easy to implement
  Doesn’t work with curved surfaces
GJK
  Works with everything
  Hard to understand
  Not hard to implement
  Hard to get contact info (EPA)
Notes: Before closing up narrow-phase I want to give a brief overview of some methods for collision detection. Most simple primitive shape tests (e.g. sphere, aabb, triangle) are commonly hand-written. There’s a ton of references for these around, but I recommend looking at the orange book (Real Time Collision Detection). For most 2D games, you’ll be fine with these.
If you start getting into more complicated tests then you might consider looking into a generic solution. There’s two methods I want to highlight here: SAT and GJK.
SAT (Separating Axis Theorem) is significantly easier to understand and fairly easy to implement but doesn’t easily work with non-polygons. GJK works with everything but is much harder to understand (not to implement). Additionally GJK won’t help when it comes to generating the contact manifold, a separate algorithm known as EPA is required.
The full details of what goes into these is well beyond the scope of this presentation. If you’re interested either talk to me, look at physics club slides, or look at some of the ‘recent’ GDC presentations on these topics (box2d website)

## Slide 20: Collision Detection - MidPhase
Turns object pairs into primitives (optional phase)
C
C
C
Notes: I won’t really talk on mid-phase much in this presentation but I want to describe it at a high-level real quick. As broad-phase spits out object pairs and narrow-phase takes in primitive pairs for individual functions we’ve written, what happens if one object is composed of multiple primitives? This is common for meshes and terrain.
The basic idea is to just have one in-between step that allows some extra pruning to happen to more efficiently pass objects to narrow-phase.

## Slide 21: Resolution
Resolves collisions given mass and contact data
  Doesn’t need colliders
Most expensive phase!
Notes: The final main phase in the physics pipeline is resolution. Resolution is where the physics engine will take the results of narrow-phase (e.g. the contact manifolds) and figures out how update velocity and position for a realistic looking collision response. This phase does not need the volume or shape information from a collider, just the mass properties and the contact manifold.
One important thing to realize about resolution is that it is by far the most expensive phase in the physics engine so it’s very important to prevent as many things as possible from getting here.

## Slide 22: Resolution
What does the resolution phase actually do?
Direction of impulse is known (the normal)
Solve for : the impulse magnitude
Notes: It can be easy to misunderstand exactly what the resolution phase’s job is. In particular, the most important thing to realize is what is actually being solved for. In almost all forms of resolution, the only thing being solved for between a pair of objects is the magnitude of the impulse which is typically referred to as . This is because the best “axis” to solve on is always known up-front. By definition, the best axis to solve a contact on (meaning the axis requiring the least work) is the axis of the normal. The only question is how strong each object should be pushed in this direction.
It can be easy to misunderstand exactly what the resolution phase’s job is. In particular, the most important thing to realize is what is actually being solved for. In almost all forms of resolution, the only thing being solved for between a pair of objects is the magnitude of the impulse which is typically referred to as 𝑗. This is because the best “axis” to solve on is always known up-front. By definition, the best axis to solve a contact on (meaning the axis requiring the least work) is the axis of the normal. The only question is how strong each object should be pushed in this direction.

## Slide 23: Resolution
Two main approaches:
Impulses:
  Easy to start
  Hard to get stable (stacking)
  Hard to represent non-contacts
Constraints
  Hard to start
  Stable
  Can represent and constraint
Notes: Resolution is commonly implemented by applying impulses (an instantaneous force) to objects to produce realistic looking collision behavior. There’s two common approaches to this nowadays: Impulses and Constraints. These approaches actually aren’t really that different when working only with contacts, but conceptually they’re quite different. There’s a lot of bad information on both of these topics floating around on the internet so I recommend being careful.

## Slide 24: Resolution
impulses constraints: they have the same
My recommendation:
Start with impulse
Do iteration with separating velocity check
Don’t do fancier impulse techniques (shock propogation)
Transition to constraints instead
Notes: The last important thing to understand about impulses vs. constraints is that they’re very close to the same thing. In particular, the impulse magnitude that is solved for is the exact same between these. The main difference is in the application of . This involves more complicated topics like warm-starting, iteration, and accumulated impulse clamping.
I recommend starting with a basic impulse engine to start any physics engine. Simply iterate over each pair and calculate and apply the impulse if the velocities aren’t separating. If this is properly set up, it’s not hard to expand to the constraint solver known as sequential impulses. These are both much larger topics so I’d recommend checking out physics club slides.
The last important thing to understand about impulses vs. constraints is that they’re very close to the same thing. In particular, the impulse magnitude that is solved for is the exact same between these. The main difference is in the application of 𝑗. This involves more complicated topics like warm-starting, iteration, and accumulated impulse clamping.
I recommend starting with a basic impulse engine to start any physics engine. Simply iterate over each pair and calculate and apply the impulse if the velocities aren’t separating. If this is properly set up, it’s not hard to expand to the constraint solver known as sequential impulses. These are both much larger topics so I’d recommend checking out physics club slides.

## Slide 25: Publish
Tell everyone else what happened
  Update transform data
  Send events
Notes: The final physics phase is where results are publish. This phase doesn’t actually involve any physics, it’s just where we tell everyone else about what physics did. The most important role is to have physics update the transform that graphics and everyone else is using since we’ve updated positions. Additionally, gameplay tends to want contact data so we send out events about collisions.

## Slide 26: Questions
Any questions so far?

## Slide 27: Recommended Implementation Order
Ignore rotation to start!
Basic setup:
Setup components/properties
Get data organized on the space
Stub 4 main phases
Notes: Now with the basics of everything described I want to give you my personal recommendation for how to tackle implementing a physics engine. There’s a lot of pieces that have to play together nicely and if you wait until there all done then it’ll be really hard to figure out what went wrong.
The first and most important thing to do when starting is to ignore rotation! Other than adding variables that you don’t yet use, I am 100% serious about this. Everything is more complicated with rotation and if you can’t get non-rotation to work first then you’re asking for trouble.
That being said, the first thing to do is to set-up the basic architecture of the engine and stub out a few things. In particular, make the basic components and their properties and get your space to have a list of these to iterate on. Once you have them then I recommend stubbing out each phase as a function call that you’ll implement later.

## Slide 28: Recommended Implementation Order
Integration:
  Apply basic forces to get objects moving
  Requires transferring data back to the engine
Notes: After this I’d recommend starting with integration. This is typically getting objects to fall with gravity. Try to get an object to fall as straight down and to also setup an initial velocity and make sure you get a good parabolic arc. This requires basic transferring of position data back to the engine for rendering too!

## Slide 29: Recommended Implementation Order
Collision detection:
  Stub BroadPhase (N-Squared)
  Simple NarrowPhase
    Spheres and boxes
Debug draw results
Only need normal and penetration to start
Notes: Afterwards I’d start with collision detection. To keep the architecture correct you’ll need to stub out a basic broad-phase here, it’s not hard to implement an n-square aabb spatial partition at this point but you can always implement a brute-force n-square (double for loop) to start.
For here you need to start implementing a basic narrow-phase. This involves getting your collision type table setup so you call the correct primitive intersection tests. I recommend starting with just spheres and aabbs (no rotation!) to start. You won’t need to generate a full manifold to start with, but you’ll need at least the contact normal and penetration distance to start.
I’d recommend doing something like changing the color or drawing the normal when two shapes are intersecting. Depending on how good of an editor you have, you can move the objects around with gizmos and try out all sorts of configurations. Otherwise I’d set-up a simple scene with no gravity and just have them fly through each other.

## Slide 30: Recommended Implementation Order
Resolution:
Start with spheres hitting without gravity
  Tests basic resolution, restitution, and mass
Move onto sphere resting on static box
  Requires penetration resolution
Add friction
  *Never do rotation before friction
Notes: Once you know you’re getting back reasonable information from collision detection you can start working on resolution. There’s a lot more subtle steps here as resolution can look very odd when partially implemented.
The first thing I’d recommend doing is getting two sphere’s to hit each other with no gravity active. You can test this with both moving or one stationary, with different sizes or mass, and with different restitution in order to verify everything seems to work as you’d expect.
Once you have this all working then you can try to move onto a resting contact with gravity. I’d recommend starting with a sphere resting on a box (you can try sphere vs. sphere if line it up perfectly). This is important because gravity will slowly drag the sphere through the box each frame so you’ll have to implement penetration resolution.
Only after you do these two things should you add friction. To test friction I’d have a ball slide along the surface of a box and make sure it slows down (and doesn’t reverse or explode). Be careful of minus signs here!
One small thing I want to point out here if you don’t follow my implementation order: if you decide to implement rotation before you have friction you’ll be very confused. Having a box rest on another box produces very weird behavior when there’s no friction. The average person has no intuition for what this should look like so you could waste a lot of time debugging something that isn’t wrong.

## Slide 31: Recommended Implementation Order
Remaining basic functionality:
  Events
  Query functions (raycasting)
Now you can do rotation (basically same order as before)
Notes: Now you should have a basic physics engine working where objects can move around, collide, and resolve. At this point I’d recommend adding the basic gameplay features the rest of your team will need to get started. In particular this is sending out events for collision detection and implementing query functions (raycasting).
It is only after this point that you should now tackle rotations. There’s another recommended implementation order for adding rotations on top of your engine, but it’s basically the exact same thing:
Integration
Detection: Requires contact points
Resolution: Same thing with no gravity and so on

## Slide 32: Debugging
Debugging Physics engines is hard
  Things often blow up in a complicated scene
  Things work most of the time, but fail horribly in unpredictable scenarios
Rule 1: Debug Drawing
Rule 2: Determinism
Rule 3: Pause/Step/Continue

## Slide 33: Debug Drawing
Helps debug a lot of data at once
Breakpoints don’t work here
Force your graphics programmer to do this right away!
Notes: One of the first things you need to debug a physics engine is debug drawing. Unlike most other systems, physics tends to do odds things in a larger scene after several frames where it’s really hard to track down the specific case that causes something to go wrong. Because of this debug drawing can be super important.

## Slide 34: Determinism
Hard to fix something you can’t reproduce
Fix your timestep (just hardcode to 1/60)
Notes: The second most important thing is to make your engine deterministic. Probably the most important rule of debugging is to get a reproduction case to a bug, but if your physics engine does something different every time you run then you’ll never be able to consistently debug. The most common thing that causes a lack of determinism is using the actual system dt. This means each frame will move objects around just a little bit differently. The easiest way to get around this is to fix your time-step, that is just hard-code it so physics always runs the same dt no matter how long it takes to run each frame. This does have some artifacts but they’re typically acceptable.
As a note, don’t do lookup the “Fix your timestep” article. If you want to discuss some of the details of this feel free, but just hardcoded your time-step and you’ll have a very good simulation.
Beyond this, there’s various things here and there that can cause a lack of determinism, but those tend to be game specific so I can’t give any generic advice.

## Slide 35: Pause/Step/Continue
If you’re deterministic bugs will happen on the same frame
Make it so you can get to a frame and look around at debug drawing in the scene
Notes: Finally, with the previous two steps we can add in pause, step, and continue logic. If you have a deterministic engine then bugs will always exhibit on the same frame (ignoring player input of course). This means you can advance to the frame before and then place breakpoints and debug the frame you care about. More commonly though, you’ll also want to be able to advance through a bad frame and look at all of the debug drawing in a scene. This means having it so you can have physics paused while you move a camera around (especially in 3D) to view all of the debug results of last frame to see if anything looks weird.

## Slide 36: Common Pitfalls
Minus signs
Space of operation
Collision Detection
Asking for help
Notes: Even with good debugging capabilities there’s a lot of common issues I’ve seen so I want to cover a few of those real quick to hopefully help you catch them early.

## Slide 37: Common Pitfalls
1. Minus signs:
  They’re everywhere and come in pairs
  Fixing one can make things look worse (when it’s more correct)
    Contact point vs. penetration distance example
  Intersection: consistent normal direction
  Can be more subtle (matrix multiplication order)
Notes: The biggest pitfall by far are minus signs. This might sound ridiculous but it’s more true than you realize. This can be something as small as a typo or as bad as flipping minus signs until things work.
The important thing to understand about minus signs is that they come in pairs. What I mean by this is that you often have to minus signs somewhere that mostly cancel each other out but not quite. This means you can have some code that’s mostly correct that occasionally blows up. When you debug it you’ll find a minus sign that you know is wrong, but fixing it makes everything worse. This means you probably had another one somewhere. I did this very thing when preparing for this presentation by accidentally flipping point A and B on the manifold. I had also flipped the penetration distance calculation to make everything work. When I tried to fix the points everything exploded because the penetration distance was wrong.
Minus signs also come in all sorts of different forms. Some are explicit minus signs while others are more subtle like matrix multiplication order (make sure you know what order to multiply your matrices in with your math library!)

## Slide 38: Common Pitfalls
2. Space of operation:
  World vs. Local space
  Make sure everything is in the correct space (label them!)
    R vectors in resolution
    Inertia tensor (3d)
    Etc…
Notes: The second most common pitfall is to not have everything in the same space when operating on it. It should be fairly obvious that you need world space values for something like collision detection, but there’s a lot of more subtle spots that are easy to forget. The most common one is the inertia tensor in 3D, but other common ones include using world space points in resolution (often you store local). The biggest recommendation I have is to name your variables explicitly so you know what space they’re operating in.

## Slide 39: Common Pitfalls
3. Collision Detection:
  90% of errors in resolution are bad data from detection ()
Make sure you spend your time debugging wisely!
Notes: There’s a joke we’ve said for a long time in physics club: 90% of errors in resolution are from detection, plus or minus 10%.
What this means is that you’ll see something explode and assume resolution has a bug. While it’s possible resolution could explode in some odd configuration, it’s more likely that detection fed resolution bad (or not good) data which causes something odd to happen. The most common of these is bad contact points causing weird torques. Make sure your contact points are on your objects!
This obviously extends to other areas of development, but be mindful that physics is like an assembly line and any previous stage could be causing an issue in a later one.

## Slide 40: Common Pitfalls
4. Asking for help:
  Ask peers!
  Ask upper-classmen!
  Ask teachers!
  Ask me (seriously)!
Ask for debugging help (try yourself first)
Ask about architecture designs
Ask about features / overscoping
Notes: The other big problem I see is being afraid to ask for help. There’s a ton of people at DigiPen who’ve made a physics engine before and have a lot of experience. One of the most important things when it comes to debugging a physics engine is intuition and you typically don’t have that when implementing your first one.
I’ve helped many people before that had an odd bug that didn’t really make sense. I looked at it and said: “I bet this data is wrong in detection, go look into it” or something akin to this. This also extends beyond bugs and into design and features. I’ve had a few people ask about how to implement a thing they want for their game and they had no idea where to look.
And seriously, I’m always available to ask. I actual really like helping people with physics!

## Slide 41: How to go from 2D to 3D
All things linear are easy
All rotations are hard (float -> Mat3):
  Inertia -> Inertia tensor (local vs. world)
  Integration (quaternions?)
  Collision detection
    Too many things to count
  Stability
*Resolution doesn’t change too much
Notes: The final thing I want to talk about is what basic information you need to go from a 2D physics engine to a 3D one. For the most part, anything that was linear (force, velocity, position) are trivial to update, simply turn a vector2 to a vector3 and most everything is done.
Unfortunately rotation isn’t so easy. The simplest thing to realize is that in 2D rotation is a single float but in 3D it becomes a matrix 3. This causes a lot of computations to get substantially more difficult.
One of the simplest complications is that the inertia also goes from a scalar to a matrix, becoming what’s called an inertia tensor. This is also more complicated as the inertia tensor changes every time the object rotates which means it needs to be updated each frame (similarity transform) from a local space inertia tensor.
Integration is also more difficult as integrating the rotation matrix will ruin the ortho-normalization of it, causing your rotations to turn into shears and scales. The easiest way to avoid this is to typically convert your rotation (for integration purposes) to a quaternion.
Collision detection is probably the worst part of going to 3D. Most tests become significantly more complicated, for instance box vs. box goes from 4 axis tests to 15. Generating contact information also becomes substantially more difficult.
All of this combines to make stability as a whole a lot harder to achieve in 3D.
That being said, resolution actually doesn’t change too much (once everything else is set-up). It’s basically another equation that just works.

## Slide 42: Questions?
Anything confusing?
Advanced things you want to know about?
Notes: Any next steps you want to know about? Good topics that don’t already have much detail could include things like kinematics or character controllers.

## Slide 43: References
Physics club: https://distance.digipen.edu/pre2012/course/view.php?id=1226
  Physics Engine Architecture
  Impulse Resolution
  Constraints Introduction
Box2d: http://box2d.org/downloads/
  Contact Creation
  Understanding Constraints
  The Separating Axis Test
  Computing Distance using GJK
CS350 slides: Ask me for them?